## Slide 1: M i s j a G O C E Przygotowania do realizacji
Janusz B. Zieliński
Zakład Geodezji Planetarnej CBK PAN
Seminarium Geodezji Satelitarnej, Poznań-Borowiec, 23-24.06.2005

## Slide 2: Grawimetryczne misje na orbitach:
CHAMP: akcelerometr, GPS, H = 450 km, i = 87˚
GRACE: SST, H = 500 km, i = 89° Sub-satellites separation ~ 200 km, Expected field resolution n ~ 100
Gravity Probe-B: H=650 km, i= 90°, supergiroskopy

## Slide 3: Projekt GOCE
GOCE – pierwsza misja gradiometryczna (2006-2007)
Orbita kołowa, wys. 250 km, i = 96˚.5 (Sun Synchr.)
Dane: 3-osiowy gradiometr: ± 10-3 EU / √Hz, orbitografia GPS
Oczekiwana rozdzielczość: n = 300

## Slide 6: Widok gradiometru

## Slide 8
Antena GPS

## Slide 9
Odbłyśnik laserowy

## Slide 10
Struktura satelity

## Slide 11: Wizja satelity GOCE w przestrzeni

## Slide 12: Główni partnerzy naukowi
  Institute for Astronomical and Physical Geodesy (IAPG) from the Technical University of Munich
· Space Research Organization Netherlands (SRON)
· The Delft Institute for Earth-Oriented Space Research (DEOS),
· French Ressources Organisation for GOCE (FROG)
· Östereichische Akademie der Wissenschaften, Institut für Weltraumforschung

## Slide 13: Komunikat z dnia 26 October 2004
Today, an important milestone was reached in the development of ESA's GOCE (Gravity field and steady-state Ocean Circulation Explorer) mission, when a contract, worth €7.8 million, was signed between ESA and the Institute for Astronomical and Physical Geodesy (IAPG) from the Technical University of Munich. The contract means that the scientific data resulting from the GOCE mission will be analysed by a consortium of 10 European universities and research institutes led by the IAPG. The consortium will then use the data to produce an unprecedented high-accuracy and high spatial-resolution global model of the Earth's gravity field and of the geoid. Scientists from Switzerland, Germany, Denmark, the Netherlands, Austria, Italy and France will all cooperate in this project. The work will be managed by IAPG as prime contractor with the help of the National Institute of Space Research in the Netherlands (SRON).

## Slide 14: Partnerzy techniczni
Main Partners
European Space Agency (ESA)
· Alenia Spazio, Torino (Prime contractor)
· EADS Astrium Friedrichshafen (Satellite constructor)
Onera: STAR Acceelerometer,
Other
· RWE Space Solar (Heilbronn): GOCE Solarpanels
· Qinetiq (GB): Ionen-Thruster
· ZARM Bremen : Magnetic Torquers for position regulation
· Marotta (Montville, New Jersey): Ventils for Ionen-Thruster
· Austrian Aerospace : Electronics for Cold-gas Thruster and thermo isolation
· ACS (Rom): Payload Data Segment (Data preprocessing)
· Deimos (Spain): Software-Validation

## Slide 15: ALENIA SPAZIO’S ROLE
As prime contractor to the European Space Agency, Alenia Spazio is responsible for the design, construction, testing and in-orbit verification of the GOCE satellite. As such, the company is co-operating with three main sub-contractors: EADS Astrium for the Service Module, Alcatel Space for the Electrostatic Gradiometer and the controlled company Laben for the GPS Receiver used as a complementary instrument. Furthermore, Alenia Spazio is responsible for designing all the pointing control and drag free algorithms and developing a functional simulator able to reproduce the generation of scientific data and predict the possible scientific performance. The company also designs and constructs the first level ground processing algorithms for the scientific data produced during the mission.

## Slide 16: ONERA -Mechanical core of the STAR accelerometer
On the basis of long experience in high resolution capacitive metrology and high-precision mechanical construction for space, the Aerospace Equipment and Instrumentation Unit has developed know-how in the measurement of very weak forces (as little as 10-15 N under certain conditions): extremely sensitive accelerometers specially designed, built, and tested for ground or space applications. These ultra-sensitive accelerometers have many possible applications in orbit, such as characterizing the micro-vibratory environment on the international space station or space shuttles, satellite orbital and attitude restoration and control, earth observation missions (gravity field, aeronomy), missions in fundamental physics in the field of relativity and gravitation.

## Slide 17: GOCE - GRAND: Hochauflösende Schwerefeldmodellierung aus Beobachtungen von GOCE für die Geowissenschaften R.Rummel, J. Flury, Th. Gruber Institutfür Astronomische undPhysikalischeGeodäsie TechnischeUniversitätMünchen

## Slide 18: Kalibrations- und Validationsstrategien für die Schwerefeldmission GOCE Jürgen Müller, Heiner Denker, Focke Jarecki, Insa Wolf Institut für Erdmessung Universität Hannover
Kalibration in zwei Schritten:
I. Fortsetzung terrestrischer Schwereanomalien nach oben
(Kleinste-Quadrate-Kollokation, Integralformeln)
II. Vergleich mit Beobachtungen und Bestimmung der
Kalibrationsparameter

## Slide 19: UCRM Upward Continuation with the Reference Model.
Geopotential models with high resolution exist (e.g. EGM 96)
A priori information may be used more directly then in collocation
Analogy to the orbit improvement approach

## Slide 20: Upward Continuation.
Enables local solutions:
FQ = UC {FP }

## Slide 23: Thank You For Your Attention